## Slide 1
ROUTING IN WIRELESS SENSOR NETWORK

## Slide 2: CONTENTS
Introduction
Routing challenges in WSN
Flat Routing
Hierarchical Routing
Location-based Routing
Routing Protocols Based on Protocol Operation
Some Other Routing protocols
Conclusion
References

## Slide 3: Introduction
Routing is a process of selecting paths in a network along which to send data traffic.
  First, it is not possible to build a global addressing scheme for a large number of sensor nodes. Thus, traditional IP-based protocols may not be applied to WSNs. In WSNs, sometimes getting the data is more important than knowing the IDs of which nodes sent the data.
  Second, in contrast to typical communication networks, almost all applications of sensor networks require the flow of sensed data from multiple sources to a particular

## Slide 4: Introduction
Routing protocols in WSNs Differ depending on the application and network architecture
Sensor nodes are tightly constrained in terms of energy, processing, and storage capacities. Thus, they require carefully resource management.
Position awareness of sensor nodes is important since data collection is normally based on the location.
Data collected by many sensors in WSNs is typically based on common phenomena, hence there is a high probability that this data has some redundancy

## Slide 5: Routing challenges and design issues
Node deployment
Energy consumption without losing accuracy
Data reporting method
Node/link heterogeneity
Scalability
Data aggregation
Quality of service

## Slide 6: Routing challenges and design issues
Node deployment
  Manual deployment
    Sensors are manually deployed
    Data is routed through predetermined path
  Random deployment
    Optimal clustering is necessary to allow connectivity & energy-efficiency
    Multi-hop routing

## Slide 7: Routing challenges and design issues
Data reporting method
  Application-specific:
    Time-driven: Periodic monitoring
    Event-driven: Respond to sudden changes
    Query-driven: Respond to queries
    Hybrid (combination of delivery models)

## Slide 8: Routing challenges and design issues
Node/link heterogeneity
Depending on the application, a sensor node can have a different role or capability such as relaying, sensing and aggregation
  Three functionalities at the same time on a node might quickly drain the energy of that node.
  Combining these capabilities on one node raises a challenge for routing protocols.
  For example, hierarchical protocols designate a cluster head node

## Slide 9: Routing challenges and design issues
Fault tolerance
  The failure of sensor nodes should not affect the overall task of the sensor network
Connectivity
  High density High connectivity
  Some sensors may die after consuming their battery power
  Connectivity depends on possibly random deployment

## Slide 10: Routing challenges and design issues
Network Dynamics
  Routing messages from or to moving nodes is more challenging since route and topology stability become important issues
  Moreover, the phenomenon can be mobile (e.g., a target detection/ tracking application).

## Slide 11: Routing challenges and design issues
Coverage
  An individual sensor’s view is limited
  Area coverage is an important design factor
Data aggregation Since sensor nodes may generate significant redundant data, similar packets from multiple nodes can be aggregated to reduce the number of transmissions.
Data aggregation is the combination of data from different sources according to a certain aggregation function.
Quality of Service
  Bounded delay
  Energy efficiency for longer network lifetime

## Slide 12: Routing Protocols in WSNs: A taxonomy

## Slide 13: On the basis of path establishment
Proactive protocols :compute all the routes before they are really needed and then store these routes in a routing table in each node. When a route changes, the change has to be propagated throughout the network. Since a WSN could consist of thousands of nodes, the routing table that each node would have to keep could be huge and therefore proactive protocols are not suited to WSNs.
Reactive protocols: compute routes only when they are needed.
Hybrid protocols: use a combination of these two ideas.

## Slide 14: Routing protocol survey
Traditional technique
Flooding
Gossiping
Current routing technique
Flat-routing
Hierarchical-routing
Location-based routing

## Slide 15: Flooding(1/4)
Flooding is the classic approach for dissemination without the need for any routing algorithms and topology maintenance
Source node sends data to all neighbors
Receiving node stores and sends data to all its neighbours
Disseminate data quickly
Drawbacks:
Implosion
Overlap
Resource blindness

## Slide 16: Implosion(2/4)

## Slide 17: Overlap(3/4)

## Slide 18: Resource blindness(4/4)
In flooding, nodes do not modify their activities based on the amount of energy available to them.
A network of embedded sensors can be resource-aware and adapt its communication and computation to the state of its energy resource.

## Slide 19: Gossiping
A slightly enhanced version of flooding where the receiving node sends the packet to a randomly selected neighbor which picks another neighbor to forward the packet to and so on.
Advantage: avoid the implosion
Drawback: Transmission delay

## Slide 20: Flat-routing (Data centric )
Each node plays the same role (Each node needs to know only its neighbours)
Data-centric routing: In data-centric routing, the sink sends queries to certain regions and waits for data from the sensors located in the selected regions.
Saves energy through data negotiation and elimination of redundant data
Protocols:
  SPIN (Sensor Protocols for Information via Negotiation)
  Directed diffusion
  Rumour routing

## Slide 21: Sensor protocols for information via negotiation (SPIN)
Features
Negotiation
  Before transmitting data, nodes negotiate with each other to overcome implosion and overlap.
  Only useful information will be transferred
  Observed data must be described using a meta-data
Resource adaptation
  Each sensor node has resource manager monitoring their own energy resources may reduce certain activities when energy is low to extend the operating lifetime of the system.
SPIN Message
  ADV – new data advertisement
  REQ – request for ADV data
  DATA – actual data message Contain actual sensor data with a meta-data header
  ADV, REQ messages contain only meta-data

## Slide 22: Sensor protocols for information via negotiation (SPIN)
Operation process

## Slide 23: Sensor protocols for information via negotiation (SPIN)
Resource adaptive algorithm
When energy is plentiful
  Communicate using the 3-stage handshake protocol
When energy is approaching a low-energy threshold
  If a node receives ADV, it does not send out REQ
  Energy is reserved to sensing the event
Advantage
  Each node only needs to know its one-hop neighbors
  Significantly reduce energy consumption compared to flooding
Drawback
  If the node interested in the data are far from the source, data will not be delivered
  Large overhead
    Data broadcasting
  Cannot guarantee delivery of data.

## Slide 24: Directed Diffusion (DD)
Feature
  Data-centric routing protocol
  A path is established between sink node and source node
  Localized interactions
    The propagation and aggregation procedures are all based on local information.
Four elements
  Interest
    A task description which is named by a list of attribute-value pairs that describe a task
  Gradient
    Path direction, data transmission rate
  Data message
  Reinforcement
    To select a single path from multiple paths

## Slide 25: Directed Diffusion (DD)
Basic scheme

## Slide 26: Directed Diffusion (DD)
Advantage
  Small delay
  Always transmit the data through shortest path
  Robust to failed path
Drawback
  Imbalance of node lifetime
    The energy of node on shortest path is drained faster than another
  Time synchronization technique
    To implement data aggregation
  Matching data to queries might require some extra overhead

## Slide 27: Rumour Routing
Variation of directed diffusion
Doesn’t flood interests (or queries)
Flood events when the number of events is small but the number of queries large
Route the query to the nodes that have observed a particular event
Long-lived packets, called agents(Set up path by random walk, Aggregate paths), flood events through the network
When a node detects an event, it adds the event to its events table, and generates an agent.
Agents travel the network to propagate info about local events.
An agent is associated with TTL

## Slide 28: Rumour Routing
Basic scheme
Each node maintain
  A lists of neighbours
  An event table
When a node detects an event
  Generates an agent
  Lets it travel on a random path
  The visited node form a gradient to the event
When a sink needs an event
  Transmit a query
  A node knowing the route to a corresponding event can respond by looking up its events table
When a node receives query
  It checks its table and returns source to destination path.

## Slide 29: Rumour Routing
No need for query flooding
Only one path between the source and sink.
Rumor routing works well only when the number of events is small.
Cost of maintaining a large number of agents and large event tables will be prohibitive.

## Slide 30: Hierarchical-routing
LEACH (Low Energy Adaptive Clustering Hierarchy)
PEGASIS (Power-Efficient Gathering in Sensor Information Systems)
TEEN(APTEEN) (Threshold-Sensitive Energy Efficient Protocols)

## Slide 31: LEACH (Low Energy Clustering Hierarchy)
Cluster-based protocol
Each node randomly decides to become a cluster heads (CH)
CH chooses the code to be used in its cluster
  CDMA between clusters
CH broadcasts ADV and each node decides, which cluster it belongs to, based on
the received signal strength of ADV.
Nodes can sleep when its not their turn to emit
CH compresses data received from the nodes in the cluster and sends the aggregated data to Base Station.
CH is rotated randomly
Cluster head
Base Station

## Slide 32: LEACH
Advantages
  Increases the lifetime of the network
  Even drain of energy
  Energy saving due to aggregation by CHs
Disadvantages
  LEACH assumes all nodes can transmit with enough power to reach BS if necessary (e.g., elected as CHs)
  Each node should support both TDMA & CDMA
  Need to do time synchronization
  Nodes use single-hop communication

## Slide 33: Comparison between SPIN, LEACH & Directed Diffusion
 | SPIN | LEACH | Directed Diffusion
Optimal Route | No | No | Yes
Network Lifetime | Good | Very good | Good
Resource Awareness | Yes | Yes | Yes
Use of meta-data | Yes | No | Yes

## Slide 34: Power-Efficient Gathering in Sensor Information Systems (PEGASIS)
Only one node transmits to BS
When a node dies, the chain is reconstructed in the same manner to bypass the dead node.
Performance:
PEGASIS Outperforms LEACH
  By eliminating the overhead of dynamic cluster formation
  By minimizing the total sum of transmission distances
  Decrease the delay for the packets during transmission to the base station
Problem
  The single leader can become a bottleneck.
  Scalability problem
  Excessive delay for distant nodes in the chain

## Slide 35: The TEEN Protocol
Threshold sensitive Energy Efficient sensor Network protocol.
Proactive Protocols (LEACH)
  The nodes in this network periodically switch on their sensors and transmitters, sense the environment and transmit the data of interest.
Reactive Protocols (TEEN)
  The nodes react immediately to sudden and drastic changes in the value of a sensed attribute.

## Slide 36: Multi-level hierarchical clustering in TEEN & APTEEN

## Slide 37: TEEN - Functioning
The cluster-head broadcasts two thresholds to its members:
  Hard Threshold (HT)
    This is a threshold value for the sensed attribute.
    It is the absolute value of the attribute beyond which, thenode sensing this value must switch on its transmitter and report to its cluster head.
  Soft Threshold (ST)
    This is a small change in the value of the sensed attribute which triggers the node to switch on its transmitter and transmit.

## Slide 38: TEEN - Hard Threshold
The first time a parameter from the attribute set reaches its hard threshold value, the node switches on its transmitter and sends the sensed data.
The sensed value is stored in an internal variable in the node, called the sensed value (SV).

## Slide 39: TEEN - Soft Threshold
The nodes will next transmit data in the current cluster period, only when both the following conditions are true:
  The current value of the sensed attribute is greater than the hard threshold.
  The current value of the sensed attribute differs from SV by an amount equal to or greater than the soft threshold.

## Slide 40: TEEN
Good for time-critical applications
If the thresholds are not reached, the user will not get any data from the network at all and will not come to know even if all the nodes die.
This scheme practical implementation would have to ensure that there are no collisions in the cluster.

## Slide 41: APTEEN (Adaptive Threshold sensitive Energy Efficient Network protocol)
APTEEN has been proposed just as an improvement to TEEN in order to overcome its limitations and shortcomings.
APTEEN guarantees lower energy dissipation and a helps in ensuring a larger number of sensors alive.
Compared to LEACH, TEEN & APTEEN consumes less energy (TEEN consumes the least)
Network lifetime: TEEN ≥ APTEEN ≥ LEACH

## Slide 42: Location-based routing
GEAR (Geographic and Energy Aware Routing)
Routing based on a cost function depending on the distance to the target and the remaining energy.
A node N receive from a neighbor Ni its cost function and then updates its own cost function:
  H(N,T) = H( Ni , T) + C(N , Ni)
If no cost function received from the node, then compute a default cost function:
  C(N,T)= αd(N,T) + (1- α) Er

## Slide 43: Geographic and Energy Aware Routing
Suppose α = 1
S is sending a packet to T
C is the closer neighbor to T
  S Sends the packet through C
S receive new learned cost function from C.
Now, B’s cost function is less than C
  Next packet will be sent through B

## Slide 44: Routing Protocols Based on Protocol Operation
Multipath Routing Protocols
Query-Based Routing
Negotiation-Based Routing Protocols
QoS-based Routing

## Slide 45: Multipath Routing Protocols
Use multiple paths in order to enhance network performance
  Fault tolerance
  Balance energy consumption
  Energy-efficient
  Reliability

## Slide 46: Query-Based Routing
Destination nodes propagate a query for data
Usually theses queries are described in natural language or high-level query language
E.g.
  Directed diffusion
  Rumour routing protocol

## Slide 47: Negotiation-Based Routing Protocols
Use high-level data descriptors in order to eliminate redundant data transmissions through negotiation
Communication decisions are also made based on the resources available to them
E.g. SPIN

## Slide 48: QoS-based Routing
Has to balance between energy consumption and data quality
E.g. SPEED (congestion avoidance)

## Slide 49
THANK YOU